## Slide 1: OUTSOURCING UTILITY COORDINATION
Oklahoma Department of Transportation
Right-of-Way & Utility Division
Marvin L. Bright, II
Manager, Utilities Branch

## Slide 2: SCOPE OF SERVICES UTILITIES
Carry out the terms of this contract in accordance with any special instructions which may be furnished by the DEPARTMENT.
Represent the DEPARTMENT’s Utility Branch on the aforementioned project regarding utility relocations and/or rearrangements in the following: written correspondence, conversations and/or field meetings with the owners/company of affected utilities. The CONTRACTOR’s decisions regarding utility relocations / rearrangements must be in accordance with existing state and federal statutes.

## Slide 3
The CONTRACTOR is expected to use sound judgment in determining the most acceptable method (for both the DEPARTMENT and the owner/company) of relocation or rearrangement of affected utilities, using due care regarding the DEPARTMENT’s betterment and/or reimbursement policy.
3. Maintain a log of all CONTRACTOR’s activities pertaining to this assignment in the form of a Monthly Progress Report. Each log entry is to contain the date, place, and description of the activity, names of other parties involved, and the time taken for the activity. See Attachment 5, Monthly Status Report, for a sample format. To furnish the DEPARTMENT with copies of the report on a monthly basis, due on the last day of each month until contract completion.
SCOPE OF SERVICES UTILITIES - cont

## Slide 4
To furnish the DEPARTMENT with copies of all correspondence handled by the CONTRACTOR on this project in accordance with Section 6, Ownership of Data. Correspondence includes notification of companies / owners, schedules of field meetings, field meeting reports, proposal / drawings and reviews.
5. To handle the following tasks:
a. Upon receipt of construction plans with cross sections, ascertains which utilities will be affected. Such work is to include site inspections of the project area to assure all affected utilities are shown on the project plans.
b. Determine each company owner's name and address.
SCOPE OF SERVICES UTILITIES - cont

## Slide 5: SCOPE OF SERVICES UTILITIES - cont
c. Provide copies of construction plans with cross sections and mail with instructions for forthcoming Field Meetings to the appropriate Division Engineer, Resident Engineer, and utility owners.
d. Receive acceptance or changes to the date and place of the Field Meetings, making any needed changes.
e. Conducts the Field Meetings (minimum of one meeting per utility owner).

## Slide 6: SCOPE OF SERVICES UTILITIES - cont
Send notices addressed to the proper Utility Owner's Official scheduling Field Meeting date and place with copies provided to the appropriate DEPARTMENT Field Division and Resident Engineer's representative. Meetings should be scheduled so that the Field Division and Resident Representatives are afforded ample opportunity to review and attend.
g. Prepare and type Field Meeting reports.
h. Mail copies of Field Meeting reports to all concerned for acknowledgment and approval, or changes. Follow up with any necessary changes to the Field Meeting reports.

## Slide 7: SCOPE OF SERVICES UTILITIES - cont
i. Submits either Proposals with detailed cost estimate and agreements, or Drawings only, during which time reminder notices may have to be sent.
j Upon receipt of Proposals and/or Drawings, reviews them for approval; obtaining revisions if necessary to meet DEPARTMENT approval.
k. Obtain signature of utility officials having contractual signatory authority on agreements.

## Slide 8: SCOPE OF SERVICES UTILITIES - cont
To attend meetings with DEPARTMENT personnel during or after completion of utility relocations / rearrangements, if requested by the DEPARTMENT.
To adhere to the following requirements:
a. Field meeting reports. Explain where the existing facility is located in relation to the centerline or survey line (feet left or right).
b. Pipelines. Show size, material, grade, and wall thickness or schedule, if plastic pipe.
c. Steel casing. List the wall thickness or lbs./ ft. of the pipeline.

## Slide 9: SCOPE OF SERVICES UTILITIES - cont
d. Parallel plastic pipe. Instruct the company that a tracer must be placed with the pipeline.
e. Telephone. List aerial or buried, pair, gauge, type of sheathing, pole height and class.
f. Fiber optic. List number of strands.
g. Steel pipe. List wall thickness, grade, lbs. /ft. and how it is protected (i.e. coated and wrapped, cathodically protected, etc.)

## Slide 10: SCOPE OF SERVICES UTILITIES - cont
h. Electric. List aerial or buried, conductor size, voltage, pole height and class, etc.
i. Rearrangements. Always include the term "in like kind" when describing the replacement unless the Company has told you they plan to upgrade their system. In which case, describe the betterment, and list it in the General Notes.
j. Placement of new facilities. Be specific regarding the placement of new facilities, such as: parallel to and four (4) feet inside the south right-of-way line, or a four-foot minimum depth below the proposed ditch flow line at Station X.

## Slide 11: SCOPE OF SERVICES UTILITIES - cont
8. Acquire latest electronic copy of Roadway Design files from the Utilities Branch.
9. Prepare or obtain Field Meeting Reports and or Utility Owner’s relocation proposals as set forth in the Utilities Branch Procedures.
10. Upon successful completion of the Field Meeting Reports, submits Preliminary "As Planned" Color Plans to the Contract Facilitator:
a. Uses latest version of Preliminary Design Construction Plans depicting proposed Right-of-Way or Easements.
b. Plots each utility owner's proposed relocations as described in the "Utility/CADD Specialist's Field Meeting Reports" on plans described in Paragraph 5(h) using APWA Uniform Color Codes.
c. Submits two (2) copies of Preliminary "As Planned" Color Plans at scale on 11"x17" sheets.

## Slide 12: SCOPE OF SERVICES UTILITIES - cont
11. Submits Final Copies of "As Planned" Color Drawings to the Contract Facilitator:
a. Acquires and uses latest version of Preliminary Design Construction Plans depicting proposed Right-of-Way or Easements, plots each Utility Owner's Proposal/Drawings on the plans described in Paragraph 10(j) using APWA Uniform Color Codes. The plotting will depict the location and placement of all parallel facilities including the exact location of all crossings. All power pole locations will be depicted as a small red dot with placement at station and distance from centerline of survey and connected with a red colored line.
12. Based on the Contract Facilitator's recommendation; makes revisions, corrections, or changes to the "As- Planned" Plans that are necessary to coincide with the field meeting reports or actual utility owner proposals.

## Slide 13: SCOPE OF SERVICES UTILITIES - cont
14. "As Planned" plans shall include a Title Sheet, Typical Sheet(s) and all Plan and Profile Sheets. (See sample provided)
a. Title Sheet shall include the "OKIE One Call" symbol and a project location map similar or identical to the location map located on the Construction Plan Title Sheet.
b. Title Sheet and Plan Sheets shall include the disclaimer: "This sheet is for INFORMATION PURPOSES ONLY. This is a compilation of the proposed utility relocation plans pertaining to the affected utility owners. The locations shown are proposed and may not reflect the current or final locations. It is still the responsibility of the Contractor and the Subcontractors to verify the actual locations of the utilities by contacting the utility owners and/or OKIE at 1-800-522-6543."
c. Plan Sheets shall include "Leader Boxes" with Utility Owner's name and defining the location with a minimum and maximum offset distance from the R/W line. Parallel facilities shall be shown with minimum and maximum offset on one Typical Section. Power Pole locations shall be depicted at the Station and Offset Distance (from centerline) provided by the owner.

## Slide 14: SCOPE OF SERVICES UTILITIES - cont
15. Electronic files shall be submitted in MicroStation version V8 or later and in PDF format on compact disc and contain the following:
a. Compact discs shall be labeled with correct Job Piece Number, Project Number, County, Highway Number, Current Date and Service Provider's name and/or Logo (see sample provided).
b. Compact Discs shall contain electronic drawings in numerical order and labeled as such: Title Sheet, Typical Sheet, Util. Plan Sht. 1, Util. Plan Sht. 2,
Util. Plan Sht. 3, etc.
c. Drawings shall have all pertinent and necessary reference files attached and necessary levels activated so that entire drawing is viewable at the initial time of opening. The drawing shall match the accompanied hard copy of "As-Planned" plans in
their entirety.

## Slide 15: SCOPE OF SERVICES UTILITIES - cont
d. Drawings shall be black background and white line work except for all proposed utility relocation information mentioned in this Scope of Services. All line work of the utility related information shall match that of the APWA standards.

## Slide 16: COMPENSATION
CONTRACTOR’s compensation under the terms of this Contract shall be the sum of _____________________ Dollars ($0,000.00) as not to exceed amount. Any other compensation shall be agreed to in writing and authorized by the DEPARTMENT.
The DEPARTMENT agrees to pay the CONTRACTOR in five installment payments. The first payment of 20% will be paid upon completion of field meetings with all affected Utility Owners. The second payment of 30% will be paid upon completion of field meeting reports and submittal of preliminary “As-Planned” plans, such completion being to the satisfaction of the DEPARTMENT’s Utilities Branch Manager. The third payment of 20% will be paid upon receipt of all company proposals/drawings. The fourth payment of 20% will be paid upon completion of the DEPARTMENT’s review, approval and acceptance of all proposals/drawings and submittal of final “As Planned” plans with electronic files on compact disc. The DEPARTMENT shall retain 10% of the amount billed until completion of all services to the satisfaction of the DEPARTMENT and the acceptance of the contract work. The fifth payment will be for the 10% retainage and any other balance due. On each of the installment payments, the CONTRACTOR is to submit a statement of services rendered.

## Slide 17: COMPENSATION
In the event the CONTRACTOR fails to meet the required completion dates, a penalty of $100.00 per utility relocation/rearrangement per calendar day, may be assessed except for good cause as shown in writing and approved through written confirmation by the DEPARTMENT. The DEPARTMENT may waive this penalty assessment or any part thereof.

## Slide 18: OWNERSHIP OF DATA
CONTRACTOR agrees to maintain current, accurate, and complete individual parcel files to the DEPARTMENT’s standards and applicable federal requirements which contain the items listed in Attachment 1, Scope of Services, and all other notes, records, correspondence, reports, and documentation generated in connection with the work called for in the Contract. All files shall be available for immediate review and inspection by any authorized DEPARTMENT or Federal Highway Administration (FHWA) official(s). All information developed under this Contract shall be the property of the DEPARTMENT and shall be delivered to the DEPARTMENT on written request, but, in any event not later than thirty (30) days following completion of the project unless otherwise set out by Attachment 2, Required Completion Dates.

## Slide 19: QUESTIONS